## Slide 2
The TeacherGeek Quick-Start Guide provides a great reference for techniques, tools and tips used to assure successful building.
Before beginning construction, take time to review this important information..
QUICK-START GUIDE
Click on this image to open the full PDF document.

## Slide 3
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S

## Slide 4
1
Using four 10-24 x 1” machine screws and hex nuts, assemble the support legs to the ends of the hole plate on both sides as shown.
Cut one dowel to 170mm (~6 ¾”). Insert into both end holes of connector strips.
2
CREATE BASE PLATFORM
Finished Bottom View
Finished Top View
Cut one 300mm connector strip into two equal 150mm pieces.

## Slide 5
4
Lay two hole plates bottom side up on a flat surface.
CREATE ROTATING ARM SUPPORT
3
Place the other hole plate over the dowels and insert the syringe mount into the hole that is down four holes from the top and in three holes from the side as shown.
Tip: Syringe mount is placed in the corner area with no dowels. Be sure to install the mount in the horizontal direction as shown.
Cut three dowels 51mm (~2”)
Insert dowels into corners as shown.
Slide one perpendicular adaptor on to the corner dowel as shown.
5
Four Holes Down
Three Holes
Over

## Slide 6
6
ATTACHING SWIVEL ARM SUPPORT TO BASE
Place 10-24 x 1” machine screw from the bottom of the base through the hole that is 9 holes over in the 2nd as shown. Place two #10 washers over the bolt.
7
Place the inside hole of the perpendicular adaptor that is mounted to the swivel arm support over the washers on the machine screw.
8
Place 10-24 locking hex nut on the screw and tighten.
Loosen the locking nut just enough so the swivel arm support can rotate freely.
2nd row
9 holes over

## Slide 7
BUILDING THE LOWER COMPONENT OF THE ARM
9
Cut three dowels 76mm (~3”).
Ream the holes on two large syringe clips.
Slide large syringe clips on two of the dowels.
To assemble as shown insert a dowel with syringe clip into the first holes on both 300mm connector strips. Now insert a dowel (without a syringe clip) into the 20th holes of the connector strips. Finally insert a dowel with a syringe clip into the 26th holes of the connector strips.
Ream the 8th hole on both connector strips as shown.
Ends of all dowels need to extend 6mm (~1/4”).
8th Hole
8th Hole
20th hole from left
26th hole
from left

## Slide 8
10
Cut two dowels 51mm (~2”).
Assemble two full connector strips with the cut dowels in the 7th and 21st holes as shown.
Dowel ends should extend beyond the connector strips by 6mm (~1/4”).
BUILDING THE UPPER COMPONENT OF THE ARM
7th hole
21st hole
Cut 45mm (~1 ¾”) off one connector strip as shown.
Extend dowels 6mm (~1/4”)
11
Any Holes
Spacing Between Upper Arm Connector Strips is 31mm (1 ¼”)

## Slide 9
JOINING THE LOWER AND UPPER ARM COMPONENTS
12
Cut one dowel 90mm (~3 1/2”).
Insert the 90mm (3 1/2”) dowel through one reamed hole (8th from end) of the lower arm section. Then into both of the unreamed 7th holes of the upper arm component. Finally insert the dowel through the reamed hole of the lower arm component.
Spacing between the upper arm connector strips should be 31mm (~1 ¼”).
Place Teacher Geek Clips on both ends of the dowel.
Lower Arm Section
Upper Arm Section
8th Hole Reamed Both Sides
Upper Arm Section
Lower Arm Section
7th Hole
Spacing Between Upper Arm Connector Strips is 31mm (1 ¼”)

## Slide 10
13
Cut one dowel 76mm (~3”).
Insert dowel through holes as shown so equal amounts of dowel extend past the hole plates.
ATTACHING ARM TO THE SWIVEL BASE
14
To attach the arm to the base insert the extending dowel ends through the 6th holes on the lower arm section.
Top hole of third vertical row in.
Both Sides

## Slide 11
15
Place syringe mount pins into the 3rd hole from the end of the upper arm component.
Press 10ml syringe into the syringe mount and slide the end of the syringe into the clip as shown.
INSTALLING 10ML SYRINGE ON ARM
3rd Hole
Syringe Mount
Any Holes

## Slide 12
INSTALLING 10ML SYRINGE IN SWIVEL BASE
16
Press 10ml syringe into the syringe mount in the swivel base and slide the end of the syringe into the clip as shown.
Syringe
Clip
Syringe
Mount

## Slide 13
INSTALLING 10ML SYRINGE IN SWIVEL BASE
17
Cut dowel 76mm (~3”).
Place in corner hole of base as shown.
18
Place 10cc syringe mount in the 3rd hole from the corner on support leg side in the vertical position as shown.
Slide a perpendicular adaptor over the dowel and onto the syringe mount pin as shown.
Third hole from corner
Any Holes

## Slide 14
INSTALLING 10ML SYRINGE ON SWIVEL BASE
19
Insert a 10-24 x 1.5” machine screw from the inside out in the 6th hole up in the first vertical row as shown.
Install a 10-24 hex nut and tighten to the hole plate.
Thread a 2nd hex nut onto the machine screw leaving a 19mm (~3/4”) space between the hex nuts.
Cut dowel 39mm (~1 ½”) and insert into the center hole of a perpendicular adaptor.
Slide an end hole of the perpendicular adaptor on the machine screw so that it contacts the hex nut.
Install another 10-24 hex nut and tighten securely on the perpendicular adaptor.
20
Ream a large syringe clip and slide over the end of a 10ml syringe.
Press syringe into the syringe mount installed on the base and slide the reamed syringe clip up on to the dowel as shown.
Syringe
Clip Hole
First vertical row
6 holes up

## Slide 15
BUILDING THE GRIPPER
21
Insert 3ml syringe into a 3ml syringe holder.
Place a 10-24 x 1” machine screw into the syringe holder and into the 4th hole of the longer connector strip of the upper arm component.
Tighten securely with a 10-24 hex nut.
22
Cut dowel 90mm (~4 ½”).
Slide the dowel in the last hole of the connector strip so that it extends 13mm (~3/4”) to the outside.
Over that 13mm (~3/4”) extension slide a perpendicular adaptor through its center hole. The dowel will still extend beyond the adaptor.

## Slide 16
FINISH BUILDING THE GRIPPER
23
Cut dowel 90mm (~3 ½”).
Slide this dowel in the end hole of a perpendicular adaptor.
Slide this dowel and adaptor into the top hole of the adaptor already installed on the gripper as shown.
24
Cut a dowel 115mm (~4 ½”).
Slide the dowel through the center hole of a perpendicular adaptor so 25mm ( 1”) extends through the other side.
Slide a small syringe clip over the other end as shown.
Ream the hole shown in the perpendicular adaptor that is closest to the syringe clip.
Slide the reamed hole of the assembly in step 20 over the gripper dowel as shown.
Install the small syringe clip over the end of the syringe.
Place a Teacher Geek Clip on the end of the dowel as shown.
25
Reamed hole
slides freely on dowel.

## Slide 17
Cut four lengths of tubing as indicated below.
CUT VINYL TUBING TO LENGTH
26
80cm (~32 in.) BASE MOUNTED ROTATING SYRINGE TUBING
80cm (~32 in.) LOWER ELEVATING SYRINGE TUBING
140cm (~54 in.) GRIPPER SYRINGE TUBING
110 cm (~42 in.) MID ARM SYRINGE TUBING

## Slide 18
27
FILLING SYRINGES AND TUBING
Keeping the end of the tubing in the water, draw a full 10ml of water into the syringe.
29
Place tubing over end of syringe and other end into the water.
Depress syringe fully to fill tubing.
28
Place fully depressed syringe into water.
Draw a full 10 ml into the syringe.
Water coloring is optional.

## Slide 19
FILLING SYRINGES AND TUBING
30
Push the mounted syringe plunger
all the way in as shown.
Place end of filled tube on to the base mounted syringe.
32
31
Push and pull the control syringe to rotate the rotating base.

## Slide 20
INSTALLING SYRINGES INTO CONTROL PANEL
Control Panel
Control Syringe
36
35
34
33
Carefully disconnect filled tubing from control syringe.
Repeat with the three remaining control syringes.
The gripper syringe is only 3ml so when filling the 10ml control syringe, stop at 3ml.
Insert syringe into a hole on control panel.
Squeezing the end of the tubing to remove any air bubbles, slide back on to the control syringe.

## Slide 21
SECURE THE TUBING TO ARM
Using twist ties or zip ties, secure the tubing to arm. Also group together the four tubes going to control panel.
37
Leave the ties slightly loose so they do not restrict the water flow through the tubes.
Be sure the tubing has enough slack so as to not restrict the movement.
IMPORTANT TIPS
Both 80cm tubing sections go from control panel to the arms lower cylinders.
80cm Tubing
110cm Tubing
140cm Tubing

## Slide 22
CREATING COUNTER BALANCE WITH RUBBER BANDS
Loop rubber bands through the end of both lower arm connector strips.
Ream the 8th hole down in the first vertical row of the hole plates (both sides).
Cut a 76mm (~3”) dowel and insert into the reamed holes.
Hook the other end of the rubber bands over the dowel ends as shown.
Loop rubber bands through the end of both upper arm connector strips.
Hook the other end of the rubber bands over the dowel extensions as shown.
8th Hole Down
38
39

## Slide 23
3
THE FINISHED HYDRAULIC ARM